## Slide 1: Evaluation of parallelism techniques on embedded multi-core platforms
Lucas Jenß
Mentor: Prof. Dr. B. Schwarz

## Slide 2: Outline
Development Platform
Parallelism Techniques
  Pipeline Pattern
  Single Instruction – Multiple Data (SIMD)
Google Go for parallelism

## Slide 3: The Platform

## Slide 5: Obstacle Detection
Using Laser scanner
  Data rate: ~34KB/s
  10Hz scanning freq.
  240° in 0.36° steps
Currently implemented using Java on Android OS
[1]

## Slide 6: Lane Guiding Control
Lane Guiding Control using high FPS camera (60 FPS, 640x480px)
Data rate: ~17.6MB/s
Pixel Clock: 27MHz
Implemented using C and RTL models, on Linux

## Slide 7
Current state: mix of different technologies
  Java on Android
  C on Linux parallel to RTL/FPGA
Goals:
  technological unification of the platform
  parallelization of tasks to improve throughput

## Slide 8: Outline
Development Platform
Parallelism Techniques
  Pipeline Pattern
  Single Instruction – Multiple Data (SIMD)
Google Go for parallelism

## Slide 9: Parallelism Techniques
Pipeline pattern

## Slide 10: Pipeline Pattern ”Assembly line” example
[2]

## Slide 11: Pipeline Pattern ”Assembly line” example
Analogy: Assembly line (e.g. for a Car)
Car #1

## Slide 12: Pipeline Pattern ”Assembly line” example
Car #2
Car #1

## Slide 13: Pipeline Pattern ”Assembly line” example
Car #3
Car #2
Car #1

## Slide 14: Pipeline Pattern ”Assembly line” example
All workers
  are busy at all times
  work on different tasks on different cars
  yet all tasks are directly related
Car #3
Car #2
Car #1

## Slide 15: Pipeline Pattern ”Assembly line” example
Assembly line has
  Workers
  Cars, or some other items
  Transport mechanism for the items

## Slide 16: Pipeline Pattern ”Assembly line” example
For the pipeline pattern, this translates to
  Threads (instead of Workers)
  Data (instead of Cars)
  Communication channel (instead of the transport mechanism)

## Slide 17: Pipeline Stage Pseudo code
while(more elements) { receive element from previous stage perform operation on element send element to the next stage }

## Slide 18: Pipeline Stage Pseudo code
while(more elements) { receive element from previous stage perform operation on element send element to the next stage }

## Slide 19: Pipeline Stage Pseudo code
while(more elements) { receive element from previous stage perform operation on element send element to the next stage }

## Slide 20: Pipeline Pattern
Theoretically:
  Parallelization of any computing problem
  Because the pipeline “transforms” linearity into parallelism

## Slide 21: Pipeline Pattern
In practice:
  Communication between stages is the bottleneck
  In order to achieve good performance:
    Communication time Stage operation time
    Small difference between stage operation times

## Slide 23: Outline
Development Platform
Parallelism Techniques
  Pipeline Pattern
  Single Instruction – Multiple Data (SIMD)
Google Go for parallelism

## Slide 24: Single Instruction – Multiple Data
Using the ARM NEON engine

## Slide 25: Single Instruction - Multiple Data
Exploits data-level parallelism
  Operations repeatedly applied to independent data

## Slide 26: Single Instruction - Multiple Data
Example: Converting an image to gray scale
  Weighted average of each pixel’s RGB values
    Sum of products
[3]

## Slide 27: Single Instruction – Single data Converting an image to gray scale
Notes: TODO:
Show each step

## Slide 28: Single Instruction – Single data Image to gray scale – Sum of products
void rgb2grey(uint8_t *dest, uint8_t *src, int pixels) { for(int i=0; i < pixels; i++) { uint8_t r = *src++; uint8_t g = *src++; uint8_t b = *src++; uint16_t y = r * 77 + g * 151 + b * 28; *dest++ = (y >> 8); } }
Notes: TODO:
Multiply
Write back

## Slide 29: Single Instruction – Single data Converting an image to gray scale
void rgb2grey(uint8_t *dest, uint8_t *src, int pixels) { for(int i=0; i < pixels; i++) { uint8_t r = *src++; uint8_t g = *src++; uint8_t b = *src++; uint16_t y = r * 77 + g * 151 + b * 28; *dest++ = (y >> 8); } }
Notes: TODO:
Multiply
Write back

## Slide 30: Single Instruction – Single data Converting an image to gray scale
void rgb2grey(uint8_t *dest, uint8_t *src, int pixels) { for(int i=0; i < pixels; i++) { uint8_t r = *src++; uint8_t g = *src++; uint8_t b = *src++; uint16_t y = r * 77 + g * 151 + b * 28; *dest++ = (y >> 8); } }
Notes: TODO:
Multiply
Write back

## Slide 31: Single Instruction – Single data Converting an image to gray scale
void rgb2grey(uint8_t *dest, uint8_t *src, int pixels) { for(int i=0; i < pixels; i++) { uint8_t r = *src++; uint8_t g = *src++; uint8_t b = *src++; uint16_t y = r * 77 + g * 151 + b * 28; *dest++ = (y >> 8); } }
Notes: TODO:
Multiply
Write back

## Slide 32: Single Instruction – Multiple data Converting an image to gray scale
ARM NEON uses special registers
  Separate from CPU registers
  “Q”(uad) and “D”(ouble), 128-bit and 64-bit wide
  Multiple elements per register
    e.g. 8 * 8 bit in “D” register

## Slide 33: Single Instruction – Multiple data Converting an image to gray scale
Steps to use SIMD:
  Load data into NEON registers
  Apply operations
  Write data back to memory

## Slide 34: Single Instruction – Multiple data Converting an image to gray scale
Steps to use SIMD:
  Load data into NEON registers
  Apply operations
  Write data back to memory

## Slide 35: Single Instruction – Multiple data Load data into NEON “D” registers

## Slide 36: Single Instruction – Multiple data Apply operations
multiply, accumulate
multiply

## Slide 37: Single Instruction – Multiple data Apply operations
multiply, accumulate
multiply

## Slide 38: Single Instruction – Multiple data Converting to gray scale
for(int i=0; i < pixels; i += FACTOR) { uint8x8x3_t rgb = vld3_u8(src); uint16x8_t acc; acc = vmull_u8(rgb.val[0], rcoeff); acc = vmlal_u8(acc, rgb.val[1], gcoeff); acc = vmlal_u8(acc, rgb.val[2], bcoeff); uint8x8_t result = vshrn_n_u16(acc, 8); vst1_u8(dest, result); src += FACTOR; dest += FACTOR; }

## Slide 39: Single Instruction – Multiple data Converting to gray scale
for(int i=0; i < pixels; i += FACTOR) { uint8x8x3_t rgb = vld3_u8(src); uint16x8_t acc; acc = vmull_u8(rgb.val[0], rcoeff); acc = vmlal_u8(acc, rgb.val[1], gcoeff); acc = vmlal_u8(acc, rgb.val[2], bcoeff); uint8x8_t result = vshrn_n_u16(acc, 8); vst1_u8(dest, result); src += FACTOR; dest += FACTOR; }
Load (3 Interleaved)

## Slide 40: Single Instruction – Multiple data Converting to gray scale
for(int i=0; i < pixels; i += FACTOR) { uint8x8x3_t rgb = vld3_u8(src); uint16x8_t acc; acc = vmull_u8(rgb.val[0], rcoeff); acc = vmlal_u8(acc, rgb.val[1], gcoeff); acc = vmlal_u8(acc, rgb.val[2], bcoeff); uint8x8_t result = vshrn_n_u16(acc, 8); vst1_u8(dest, result); src += FACTOR; dest += FACTOR; }
uint8x8x3_t
Type
Elements per Register
# of Registers

## Slide 41: Single Instruction – Multiple data Converting to gray scale
for(int i=0; i < pixels; i += FACTOR) { uint8x8x3_t rgb = vld3_u8(src); uint16x8_t acc; acc = vmull_u8(rgb.val[0], rcoeff); acc = vmlal_u8(acc, rgb.val[1], gcoeff); acc = vmlal_u8(acc, rgb.val[2], bcoeff); uint8x8_t result = vshrn_n_u16(acc, 8); vst1_u8(dest, result); src += FACTOR; dest += FACTOR; }
Loads 8bit * 8 * 3 = 192 bit = 24 byte!

## Slide 42: Single Instruction – Multiple data Converting to gray scale
for(int i=0; i < pixels; i += FACTOR) { uint8x8x3_t rgb = vld3_u8(src); uint16x8_t acc; acc = vmull_u8(rgb.val[0], rcoeff); acc = vmlal_u8(acc, rgb.val[1], gcoeff); acc = vmlal_u8(acc, rgb.val[2], bcoeff); uint8x8_t result = vshrn_n_u16(acc, 8); vst1_u8(dest, result); src += FACTOR; dest += FACTOR; }
Apply
operations

## Slide 43: Single Instruction – Multiple data Converting to gray scale
for(int i=0; i < pixels; i += FACTOR) { uint8x8x3_t rgb = vld3_u8(src); uint16x8_t acc; acc = vmull_u8(rgb.val[0], rcoeff); acc = vmlal_u8(acc, rgb.val[1], gcoeff); acc = vmlal_u8(acc, rgb.val[2], bcoeff); uint8x8_t result = vshrn_n_u16(acc, 8); vst1_u8(dest, result); src += FACTOR; dest += FACTOR; }
Multiply

## Slide 44: Single Instruction – Multiple data Converting to gray scale
for(int i=0; i < pixels; i += FACTOR) { uint8x8x3_t rgb = vld3_u8(src); uint16x8_t acc; acc = vmull_u8(rgb.val[0], rcoeff); acc = vmlal_u8(acc, rgb.val[1], gcoeff); acc = vmlal_u8(acc, rgb.val[2], bcoeff); uint8x8_t result = vshrn_n_u16(acc, 8); vst1_u8(dest, result); src += FACTOR; dest += FACTOR; }
Multiply +
Accumulate

## Slide 45: Single Instruction – Multiple data Converting to gray scale
for(int i=0; i < pixels; i += FACTOR) { uint8x8x3_t rgb = vld3_u8(src); uint16x8_t acc; acc = vmull_u8(rgb.val[0], rcoeff); acc = vmlal_u8(acc, rgb.val[1], gcoeff); acc = vmlal_u8(acc, rgb.val[2], bcoeff); uint8x8_t result = vshrn_n_u16(acc, 8); vst1_u8(dest, result); src += FACTOR; dest += FACTOR; }
Shift Right

## Slide 46: Single Instruction – Multiple data Converting to gray scale
for(int i=0; i < pixels; i += FACTOR) { uint8x8x3_t rgb = vld3_u8(src); uint16x8_t acc; acc = vmull_u8(rgb.val[0], rcoeff); acc = vmlal_u8(acc, rgb.val[1], gcoeff); acc = vmlal_u8(acc, rgb.val[2], bcoeff); uint8x8_t result = vshrn_n_u16(acc, 8); vst1_u8(dest, result); src += FACTOR; dest += FACTOR; }
Write back to memory

## Slide 47: Single Instruction – Multiple data Converting to gray scale
for(int i=0; i < pixels; i += FACTOR) { uint8x8x3_t rgb = vld3_u8(src); uint16x8_t acc; acc = vmull_u8(rgb.val[0], rcoeff); acc = vmlal_u8(acc, rgb.val[1], gcoeff); acc = vmlal_u8(acc, rgb.val[2], bcoeff); uint8x8_t result = vshrn_n_u16(acc, 8); vst1_u8(dest, result); src += FACTOR; dest += FACTOR; }
FACTOR = # of elements
processed per iteration (24)

## Slide 48: Single Instruction – Multiple data Performance
Native C-Version
  16 Instructions / Pixel
SIMD Version:
  15 Instructions / 8 Pixels
  ~2 Instructions / Pixel

## Slide 50: Outline
Development Platform
Parallelism Techniques
  Pipeline Pattern
  Single Instruction – Multiple Data (SIMD)
Google Go for parallelism

## Slide 51: Google Go
for parallel applications

## Slide 52: Google Go
A programming language that is
  simple
  compiled
  built with concurrency in mind

## Slide 53: Language Specification Who’s keeping it simple?
Image courtesy of Marian Tietz
“Google Go – An Introduction”

## Slide 54: Google Go Concurrency as a language feature
Go-Routines (go keyword)
  lightweight threads scheduled by the Go runtime
  concurrently execute any function
  sequential execution:
  function(parameter1, parameterN…)

## Slide 55: Google Go Concurrency as a language feature
Go-Routines (go keyword)
  lightweight threads scheduled by the Go runtime
  concurrently execute any function
  concurrent execution:
  go function(parameter1, parameterN…)

## Slide 56: Google Go Concurrency as a language feature
Channels
  first-class value (i.e. handled as a primitive)
  thread-safe communication mechanism
  buffered / unbuffered

## Slide 57: Google Go Concurrency as a language feature
Channels
  create channel
  chan := make(chan int)

## Slide 58: Google Go Concurrency as a language feature
Channels
  send data to channel
  chan <- 5

## Slide 59: Google Go Concurrency as a language feature
Channels
  retrieve data from channel
  value := <- chan

## Slide 60: Code example Pipeline pattern in Go!

## Slide 61: Code example Pipeline pattern in Go!
func main() { stage1_in := make(chan int) stage1_out := make(chan int) go func() { for _, element := range [4]int{1, 2, 3, 4} { stage1_in <- element } }() go stage1(stage1_in, stage1_out) go stage2(stage1_out, nil) }

## Slide 62: Code example Pipeline pattern in Go!
func main() { stage1_in := make(chan int) stage1_out := make(chan int) go func() { for _, element := range [4]int{1, 2, 3, 4} { stage1_in <- element } }() go stage1(stage1_in, stage1_out) go stage2(stage1_out, nil) }

## Slide 63: Code example Pipeline pattern in Go!
func main() { stage1_in := make(chan int) stage1_out := make(chan int) go func() { for _, element := range [4]int{1, 2, 3, 4} { stage1_in <- element } }() go stage1(stage1_in, stage1_out) go stage2(stage1_out, nil) }

## Slide 64: Code example Pipeline pattern in Go!
func main() { stage1_in := make(chan int) stage1_out := make(chan int) go func() { for _, element := range [4]int{1, 2, 3, 4} { stage1_in <- element } }() go stage1(stage1_in, stage1_out) go stage2(stage1_out, nil) }

## Slide 65: Code example Pipeline pattern in Go!
func stage1(in chan int, out chan int) { for { current := <- in op := current * 2 out <- op } } func stage2(in chan int, out chan int) { for { current := <- in fmt.Println("Value: ", current) } }

## Slide 66: Code example Pipeline pattern in Go!
func stage1(in chan int, out chan int) { for { current := <- in op := current * 2 out <- op } } func stage2(in chan int, out chan int) { for { current := <- in fmt.Println("Value: ", current) } }
Read data from channel

## Slide 67: Code example Pipeline pattern in Go!
func stage1(in chan int, out chan int) { for { current := <- in op := current * 2 out <- op } } func stage2(in chan int, out chan int) { for { current := <- in fmt.Println("Value: ", current) } }
Perform operation

## Slide 68: Code example Pipeline pattern in Go!
func stage1(in chan int, out chan int) { for { current := <- in op := current * 2 out <- op } } func stage2(in chan int, out chan int) { for { current := <- in fmt.Println("Value: ", current) } }
Send data to next stage’s channel

## Slide 69: Code example Pipeline pattern in Java…

## Slide 70: Code example Pipeline pattern in Java…
import java.util.ArrayList; import java.util.List; public interface Pipeline extends Stage { public void addStage ( Stage stage); public void addErrorStage (Stage stage); public void addFinalStage (Stage stage); } public interface PipelineContext { public List<Error> getErrors (); } public class PipelineContextAdaptor implements PipelineContext { private List<Error> m_errors = new ArrayList<Error> (); public List<Error> getErrors() { return m_errors; } public void addError (Error e){ m_errors.add(e); } }
public interface Stage { public void execute (PipelineContext context); }
public class SequentialPipeline implements Pipeline { private List<Stage> m_stages = new ArrayList<Stage> (); private List<Stage> m_errorStages= new ArrayList<Stage> (); private List<Stage> m_finalStages= new ArrayList<Stage> (); public void addStage(Stage stage) { m_stages.add(stage); } public void addErrorStage(Stage stage) { m_errorStages.add(stage); } public void addFinalStage(Stage stage) { m_finalStages.add(stage); } public void execute(PipelineContext context) { for (Stage stage:m_stages){ stage.execute(context); if (context.getErrors()!= null && !context.getErrors().isEmpty(){ break; } } if (context.getErrors()!= null && !context.getErrors().isEmpty()){ for (Stage errorStage: m_errorStages){ errorStage.execute(context); } } for (Stage finalStage: m_finalStages){ finalStage.execute(context); } } }

## Slide 71: Google Go Can we use it on embedded platforms?
We’ve seen that Go
  allows for quicker development due to less boilerplate
    simple syntax – few corner cases

## Slide 72: Google Go Can we use it on embedded platforms?
We’ve seen that Go
  is great for building parallel applications
    channels as a language feature
    go-routines (lightweight threads) as a language feature
    compiler/runtime knows these features, can find errors

## Slide 73: Google Go Can we use it on embedded platforms?
Go Concurrency
  Straightforward implementation of the pipeline pattern
  But other concurrency patterns work great too
    Actors
    Fork/Join
    Master/Worker

## Slide 74: Google Go Can we use it on embedded platforms?
But: simplicity comes at a cost
Therefore, the question is
  How big is the performance impact of using Go on embedded system?
  And ultimately: Do the advantages of Go outweigh said performance impact?

## Slide 75: Next Milestones

## Slide 76: Next Milestones
Technological unification on Linux
  Determine if Go is a viable alternative to C
Re-implementation of obstacle detection in Go or C
    Pipeline Pattern and SIMD for throughput optimization

## Slide 77: The Big Picture

## Slide 78: The Big Picture
Processing pipeline distributed to multiple cores
Some stages use SIMD
Go Runtime schedules the go-routines

## Slide 79: The End
Any questions?

## Slide 80: References
FAUST Project (2013). FAUST - Fahrerassistenz und autonome Systeme. URL: http://faust.informatik.haw-hamburg.de (last accessed: 2013-05-07)
Kejariwal, A., Veidenbaum, A. V., Nicolau, A., Girkar, M., Tian, X. and Saito, H. (2009). On the exploitation of loop-level parallelism in embedded applications, ACM Transac- tions on Embedded Computing Systems 8(2): 1–34. ISSN: 15399087. URL: http://portal.acm.org/citation.cfm?doid=1457255.1457257
Mattson, T. G., Sanders, B. A. and Massingill, B. L. (2010). Patterns for Parallel Pro- gramming, 6th edn, Addison-Wesley, Westford, Massachusetts. ISBN: 0-321-22811- 1.
Pike, R. (2012). Go at Google, Proceedings of the 3rd annual conference on Systems, programming, and applications: software for humanity - SPLASH ’12 p. 5. URL: http://dl.acm.org/citation.cfm?doid=2384716.2384720
Preud’Homme, T., Sopena, J., Thomas, G. and Folliot, B. (2012). An Improvement of OpenMP Pipeline Parallelism with the BatchQueue Algorithm, 2012 IEEE 18th International Conference on Parallel and Distributed Systems (i): 348–355. URL: http://ieeexplore.ieee.org/lpdocs/epic03/wrapper.htm?arnumber= 6413677

## Slide 81: Images
[1] URL:
http://de.manu-systems.com/URG-04LX-UG01.shtml (last accessed on 2013-06-02)
[2] URL: http://www.wall321.com/Cars/Volkswagen/cars_vehicles_volkswagen_1280x800_wallpaper_44233/download_1920x1200 (last accessed on 2013-05-21)
[3] URL:
http://www.wallpaperdev.com/wallpaper/1600x1200/cute-cat-by-ashish-8511.html (last accessed on 2013-06-03)