## Slide 1: Evaluation of parallelism techniques on embedded multi-core platforms
Lucas Jenß
Mentor: Prof. Dr. B. Schwarz

## Slide 2: Outline
Development Platform
Parallelism Techniques
  Pipeline Pattern
  Single Instruction – Multiple Data (SIMD)
Google Go for parallelism

## Slide 3: The Platform
Xilinx Zynq w/ Dual Core ARM CPU

## Slide 4: The Platform
Zynq 7020 SoC: ZedBoard
  Dual Core ARM with 667MHz Core Frequency
  512MB DDR3-1066 RAM
  USB/HDMI/Audio/Ethernet/…

## Slide 5: Obstacle Detection
Using Laser scanner
  Data rate: ~34KB/s
  10Hz scanning freq.
  240° in 0.36° steps
Currently implemented with Java on Android OS

## Slide 6: Lane Guiding Control
Lane Guiding Control using high FPS camera (60 FPS, 752x40px)
Data rate: ~20MB/s
Implemented using C and FPGA modules, on Linux

## Slide 8
Current state: mix of different technologies
  Java on Android, C/FPGA on Linux
Goals:
  technological unification of the platform
  parallelization of tasks to improve performance

## Slide 9: Outline
Development Platform
Parallelism Techniques
  Pipeline Pattern
  Single Instruction – Multiple Data (SIMD)
Google Go for parallelism

## Slide 10: Parallelism Techniques
Pipeline pattern

## Slide 11: Parallelism
Finding exploitable concurrency
  sub-problems that can safely execute at the same time

## Slide 12: Pipeline Pattern ”Assembly line” example

## Slide 13: Pipeline Pattern ”Assembly line” example
Analogy: Assembly line (e.g. for a Car)

## Slide 14: Pipeline Pattern ”Assembly line” example
Car #1

## Slide 15: Pipeline Pattern ”Assembly line” example
Car #2
Car #1

## Slide 16: Pipeline Pattern ”Assembly line” example
Car #3
Car #2
Car #1

## Slide 17: Pipeline Pattern ”Assembly line” example
All workers
  are busy at all times
  work on different tasks on different cars
  yet all tasks are directly related
Car #3
Car #2
Car #1

## Slide 18: Pipeline Pattern ”Assembly line” example
Assembly line has
  Workers
  Cars, or some other items
  Transport mechanism for the items

## Slide 19: Pipeline Pattern ”Assembly line” example
For the pipeline pattern, this translates to
  Threads (instead of Workers)
  Data (instead of Cars)
  Communication channel (instead of the transport mechanism)

## Slide 20: Pipeline Stage Pseudo code
while(more elements) { receive element from previous stage perform operation on element send element to the next stage }

## Slide 21: Pipeline Stage Pseudo code
while(more elements) { receive element from previous stage perform operation on element send element to the next stage }

## Slide 22: Pipeline Stage Pseudo code
while(more elements) { receive element from previous stage perform operation on element send element to the next stage }

## Slide 23: Pipeline Stage Pseudo code
while(more elements) { receive element from previous stage perform operation on element send element to the next stage }

## Slide 24: Pipeline Pattern
Theoretically:
  Parallelization of any computing problem
  Because the pipeline “transforms” linearity into parallelism

## Slide 25: Pipeline Pattern
In practice:
  Communication between stages is the bottleneck
  In order to achieve good performance:
    Communication time Stage operation time
    Small difference between stage operation times

## Slide 26: Outline
Development Platform
Parallelism Techniques
  Pipeline Pattern
  Single Instruction – Multiple Data (SIMD)
Google Go for parallelism

## Slide 27: Single Instruction – Multiple Data
Using the ARM NEON engine

## Slide 28: Single Instruction - Multiple Data
Exploits data-level parallelism
  Operations repeatedly applied to independent data

## Slide 29: Single Instruction - Multiple Data
Exploits data-level parallelism
  Operations repeatedly applied to independent data

## Slide 30: Single Instruction – Single data Converting an image to gray scale
Notes: TODO:
Show each step

## Slide 31: Single Instruction – Single data Converting an image to gray scale
void rgb2grey(uint8_t *dest, uint8_t *src, int pixels) { for(int i=0; i < pixels; i++) { uint8_t r = *src++; uint8_t g = *src++; uint8_t b = *src++; uint16_t y = r * 77 + g * 151 + b * 28; *dest++ = (y >> 8); } }
Notes: TODO:
Multiply
Write back

## Slide 32: Single Instruction – Single data Converting an image to gray scale
void rgb2grey(uint8_t *dest, uint8_t *src, int pixels) { for(int i=0; i < pixels; i++) { uint8_t r = *src++; uint8_t g = *src++; uint8_t b = *src++; uint16_t y = r * 77 + g * 151 + b * 28; *dest++ = (y >> 8); } }
Notes: TODO:
Multiply
Write back

## Slide 33: Single Instruction – Single data Converting an image to gray scale
void rgb2grey(uint8_t *dest, uint8_t *src, int pixels) { for(int i=0; i < pixels; i++) { uint8_t r = *src++; uint8_t g = *src++; uint8_t b = *src++; uint16_t y = r * 77 + g * 151 + b * 28; *dest++ = (y >> 8); } }
Notes: TODO:
Multiply
Write back

## Slide 34: Single Instruction – Single data Converting an image to gray scale
void rgb2grey(uint8_t *dest, uint8_t *src, int pixels) { for(int i=0; i < pixels; i++) { uint8_t r = *src++; uint8_t g = *src++; uint8_t b = *src++; uint16_t y = r * 77 + g * 151 + b * 28; *dest++ = (y >> 8); } }
Notes: TODO:
Multiply
Write back

## Slide 35: Single Instruction – Multiple data Converting an image to gray scale
ARM NEON uses special registers
  Separate from CPU registers
  “Q”(uad) and “D”(ouble), 128-bit and 64-bit wide
  Multiple elements per register
    e.g. 8 * 8 bit in “D” register

## Slide 36: Single Instruction – Multiple data Converting an image to gray scale
Steps to use SIMD:
  Load data into NEON registers
  Apply operations
  Write data back to memory

## Slide 37: Single Instruction – Multiple data Load data into NEON registers

## Slide 38: Single Instruction – Multiple data Apply operations
multiply, accumulate
multiply

## Slide 39: Single Instruction – Multiple data Converting to gray scale
for(int i=0; i < pixels; i += FACTOR) { uint8x8x3_t rgb = vld3_u8(src); uint16x8_t acc; acc = vmull_u8(rgb.val[0], rcoeff); acc = vmlal_u8(acc, rgb.val[1], gcoeff); acc = vmlal_u8(acc, rgb.val[2], bcoeff); uint8x8_t result = vshrn_n_u16(acc, 8); vst1_u8(dest, result); src += FACTOR; dest += FACTOR; }

## Slide 40: Single Instruction – Multiple data Converting to gray scale
for(int i=0; i < pixels; i += FACTOR) { uint8x8x3_t rgb = vld3_u8(src); uint16x8_t acc; acc = vmull_u8(rgb.val[0], rcoeff); acc = vmlal_u8(acc, rgb.val[1], gcoeff); acc = vmlal_u8(acc, rgb.val[2], bcoeff); uint8x8_t result = vshrn_n_u16(acc, 8); vst1_u8(dest, result); src += FACTOR; dest += FACTOR; }
Load (3 Interleaved)

## Slide 41: Single Instruction – Multiple data Converting to gray scale
for(int i=0; i < pixels; i += FACTOR) { uint8x8x3_t rgb = vld3_u8(src); uint16x8_t acc; acc = vmull_u8(rgb.val[0], rcoeff); acc = vmlal_u8(acc, rgb.val[1], gcoeff); acc = vmlal_u8(acc, rgb.val[2], bcoeff); uint8x8_t result = vshrn_n_u16(acc, 8); vst1_u8(dest, result); src += FACTOR; dest += FACTOR; }
uint8x8x3_t
Type
Elements per Register
# of Registers

## Slide 42: Single Instruction – Multiple data Converting to gray scale
for(int i=0; i < pixels; i += FACTOR) { uint8x8x3_t rgb = vld3_u8(src); uint16x8_t acc; acc = vmull_u8(rgb.val[0], rcoeff); acc = vmlal_u8(acc, rgb.val[1], gcoeff); acc = vmlal_u8(acc, rgb.val[2], bcoeff); uint8x8_t result = vshrn_n_u16(acc, 8); vst1_u8(dest, result); src += FACTOR; dest += FACTOR; }
Loads 8bit * 8 * 3 = 192 bit = 24 byte!

## Slide 43: Single Instruction – Multiple data Converting to gray scale
for(int i=0; i < pixels; i += FACTOR) { uint8x8x3_t rgb = vld3_u8(src); uint16x8_t acc; acc = vmull_u8(rgb.val[0], rcoeff); acc = vmlal_u8(acc, rgb.val[1], gcoeff); acc = vmlal_u8(acc, rgb.val[2], bcoeff); uint8x8_t result = vshrn_n_u16(acc, 8); vst1_u8(dest, result); src += FACTOR; dest += FACTOR; }
Apply
operations

## Slide 44: Single Instruction – Multiple data Converting to gray scale
for(int i=0; i < pixels; i += FACTOR) { uint8x8x3_t rgb = vld3_u8(src); uint16x8_t acc; acc = vmull_u8(rgb.val[0], rcoeff); acc = vmlal_u8(acc, rgb.val[1], gcoeff); acc = vmlal_u8(acc, rgb.val[2], bcoeff); uint8x8_t result = vshrn_n_u16(acc, 8); vst1_u8(dest, result); src += FACTOR; dest += FACTOR; }
Write back to memory

## Slide 45: Single Instruction – Multiple data Performance
Native C-Version
  16 Instructions / Pixel
SIMD Version:
  15 Instructions / 8 Pixels
  ~2 Instructions / Pixel

## Slide 46: Outline
Development Platform
Parallelism Techniques
  Pipeline Pattern
  Single Instruction – Multiple Data (SIMD)
Google Go for parallelism

## Slide 47: Google Go
for parallel applications

## Slide 48: Google Go What is it?
A programming language that is
  compiled
  statically typed
  not object oriented
  built with concurrency in mind

## Slide 49: Language Specification Who’s keeping it simple?

## Slide 50: Language Specification Who’s keeping it simple?
Image courtesy of Marian Tietz
“Google Go – An Introduction”

## Slide 51: Google Go Why do we want it?
It is simple!
It has built-in concurrency

## Slide 52: Code example Pipeline pattern in Go!
func main() { stage1_in := make(chan int) stage1_out := make(chan int) go func() { for _, element := range [4]int{1, 2, 3, 4} { stage1_in <- element } }() go stage1(stage1_in, stage1_out) go stage2(stage1_out, nil) }

## Slide 53: Code example Pipeline pattern in Go!
func main() { stage1_in := make(chan int) stage1_out := make(chan int) go func() { for _, element := range [4]int{1, 2, 3, 4} { stage1_in <- element } }() go stage1(stage1_in, stage1_out) go stage2(stage1_out, nil) }

## Slide 54: Code example Pipeline pattern in Go!
func main() { stage1_in := make(chan int) stage1_out := make(chan int) go func() { for _, element := range [4]int{1, 2, 3, 4} { stage1_in <- element } }() go stage1(stage1_in, stage1_out) go stage2(stage1_out, nil) }

## Slide 55: Code example Pipeline pattern in Go!
func main() { stage1_in := make(chan int) stage1_out := make(chan int) go func() { for _, element := range [4]int{1, 2, 3, 4} { stage1_in <- element } }() go stage1(stage1_in, stage1_out) go stage2(stage1_out, nil) }

## Slide 56: Code example Pipeline pattern in Go!
func stage1(in chan int, out chan int) { for { current := <- in op := current * 2 out <- op } } func stage2(in chan int, out chan int) { for { current := <- in fmt.Println("Value: ", current) } }

## Slide 57: Code example Pipeline pattern in Go!
func stage1(in chan int, out chan int) { for { current := <- in op := current * 2 out <- op } } func stage2(in chan int, out chan int) { for { current := <- in fmt.Println("Value: ", current) } }
Read data from channel

## Slide 58: Code example Pipeline pattern in Go!
func stage1(in chan int, out chan int) { for { current := <- in op := current * 2 out <- op } } func stage2(in chan int, out chan int) { for { current := <- in fmt.Println("Value: ", current) } }
Perform operation

## Slide 59: Code example Pipeline pattern in Go!
func stage1(in chan int, out chan int) { for { current := <- in op := current * 2 out <- op } } func stage2(in chan int, out chan int) { for { current := <- in fmt.Println("Value: ", current) } }
Send data to next stage’s channel

## Slide 60: Code example Pipeline pattern in Java…

## Slide 61: Code example Pipeline pattern in Java…
import java.util.ArrayList; import java.util.List; public interface Pipeline extends Stage { public void addStage ( Stage stage); public void addErrorStage (Stage stage); public void addFinalStage (Stage stage); } public interface PipelineContext { public List<Error> getErrors (); } public class PipelineContextAdaptor implements PipelineContext { private List<Error> m_errors = new ArrayList<Error> (); public List<Error> getErrors() { return m_errors; } public void addError (Error e){ m_errors.add(e); } }
public interface Stage { public void execute (PipelineContext context); }
public class SequentialPipeline implements Pipeline { private List<Stage> m_stages = new ArrayList<Stage> (); private List<Stage> m_errorStages= new ArrayList<Stage> (); private List<Stage> m_finalStages= new ArrayList<Stage> (); public void addStage(Stage stage) { m_stages.add(stage); } public void addErrorStage(Stage stage) { m_errorStages.add(stage); } public void addFinalStage(Stage stage) { m_finalStages.add(stage); } public void execute(PipelineContext context) { for (Stage stage:m_stages){ stage.execute(context); if (context.getErrors()!= null && !context.getErrors().isEmpty(){ break; } } if (context.getErrors()!= null && !context.getErrors().isEmpty()){ for (Stage errorStage: m_errorStages){ errorStage.execute(context); } } for (Stage finalStage: m_finalStages){ finalStage.execute(context); } } }

## Slide 62: Google Go Can we use it on embedded platforms?
We’ve seen that Go
  allows for quicker development due to less boilerplate
    simple syntax – few corner cases

## Slide 63: Google Go Can we use it on embedded platforms?
We’ve seen that Go
  is great for building parallel applications
    channels as a language feature
    goroutines (lightweight threads) as a language feature
    compiler/runtime know these features, can find errors

## Slide 64: Google Go Can we use it on embedded platforms?
But: simplicity comes at a cost
Therefore, the question is
  How big is the performance impact of using Go on embedded system?
  And ultimately: Do the advantages of Go outweigh said performance impact?

## Slide 65: Add Outro
Things discussed
Summary of goals

## Slide 66: The End
Any questions?